Attn:

Date:

VG510SA

Clausing 20” Semi Automatic Vertical Hydraulic Tilt Frame Miter Bandsaw

# Quotation

3963 Emerald Drive, Kalamazoo, MI 49001  Phone: 269-345-7155  Fax: 269-345-5945

###### Clausing Kalamazoo Tilt Frame Miter Bandsaw Features

- Great versatility, fast and easy set-up…The saw frame hydraulically tilts to any angle between 60( left and 60( right from control panel.  High and low frame travel speeds for exact positioning of the miter angle

- Large cutting capacity…20” x 26.4” at 90(, 20” x 18.3” at 45( left and 20” x 12.8” 60( left. Right hand tilt optional.

- Front mounted control panel…Easily control all sawing functions, miter angle, blade speed, etc.

- Fast and accurate miter settings…Digital display of miter angle with an accuracy of 0.1(

- Cutting control…Infinitely variable hydraulic cutting pressure controlled from control panel

- Canted saw frame…Saw frame can be adjusted from 0( to 5( forward for more efficient cutting of structural materials

- Large work area…By removing the movable front vise jaw, large bulky parts or irregular shaped work pieces can be manually clamped to the large work table

- Easy loading and unloading…Saw frame moves behind fixed back vise jaw to allow easy loading and unloading of workpiece from top or side

- Precision guidance…Precision saw bow guided by solid carbide blade guides with rollers along with a very rigid frame design and guided by two linear guides to guarantee very precise cuts

- Blade tension control…Equipped with hydraulic blade tension with pressure indicator

- Small footprint…For such a large cutting area the machine requires only a 98.4” x 102.36” footprint

- Flood coolant…Equipped with a recirculating flood coolant system

- Hydraulic Clamping…through rack gear

###### Clausing Kalamazoo Tilt Frame Miter Bandsaw Standard Equipment

- Powerful 7.5 hp drive motor

- Inverter variable speed drive

- Hydraulic blade tension with pressure indicator

- Digital display of miter angle, 0.1( accuracy

- Flood coolant system

- Solid carbide blade guides

- Operational and parts manual

- Left Side and Right Side Hydraulic Power Vise

Clausing Kalamazoo Tilt Frame Miter Bandsaw Specifications

| VG510SA | 0( Frame Cant | 5( Frame Cant |
| --- | --- | --- |
| Cutting Capacity | 90 Deg | 20” x 26.4” | 20” x 24” |
|  | 45 Deg Left | 20” x 18.3” | 20” x 16.7” |
|  | 60 Deg Left | 20” x 12.8” | 20” x 11.8” |
|  | 45 Deg Right | 20” x 17.1” | 20” x 15.7” |
|  | 60 Deg Right | 20” x 10.4” | 20” x 10” |
| Maximum Vise Opening | 20” |
| Blade Speed | 66 – 264 ft/min Inverter Controlled |
| Blade Size | 192.1” x 1.25” x .043” |
| Blade Tension | Hydraulic Controlled |
| Blade Guide | Interchangeable Tungsten Carbide w/ Rollers |
| Guide Arm | Hydraulic Positioning on Linear Guide |
| Saw Blade Motor | 7.5 Hp |
| Hydraulic Motor | 1 Hp |
| Hydraulic Tank Capacity | (DTE 24) 22.1 Gallons |
| Hydraulic Output Pressure | 540 – 640 PSI |
| Coolant Pump Motor | ¼ Hp |
| Coolant Tank Capacity | 34 Gallons |
| Feed Range | 0-132 lb/f |
| Work Table Size |  |
| Work Table Height | 39.4” |
| Floor Space (W x D x H) | 98.5” x 102.4” x 98.5” |
| Shipping Dim (W x D x H) |  |
| Net Weight |  |
| Shipping Weight – L x W x H |  |

All specifications are subject to change without notice or obligation.

Investment

### Clausing Kalamazoo Tilt Frame Miter Bandsaw

VG510SA	20” Heavy-Duty Hydraulic Semi-Automatic NC	$ 29,995.00 		Tilt Frame Vertical Saw Left and Right Side			Hydraulic Vise

Optional Equipment

SA24T	21” x 10’ (31” – 39”) Heavy Duty Roller Table	$ 2,255.00

SA25T	21” x 10’ (31” – 39”) Heavy Duty Roller Table	1,635.00

SA26T	25” x 10’ (31” – 39”) Heavy Duty Roller Table	2,455.00

SA27T	25” x 5’ (31” – 39”) Heavy Duty Roller Table	1,765.00

NOTE: These tables will need 4x4x½” riser plates			for the table legs. 6Pcs 10’ table, 4pcs 5’ table

Warranty

KALAMAZOO SAW WARRANTY STATEMENT:

Each KALAMAZOO Saw is WARRANTEED to be free from defects in materials and/or workmanship for a period to TWO YEARS from the date of installation.  This WARRANTY is LIMITED to factory defects and specifically excludes items subject to normal wear including the saw blade, blade brush, vise cam nut and drive belt.  Moreover this warranty only applies to machines which have been installed and operated in accordance with the instructions given in the KALAMAZOO Operation & Service Manual which is provided with each and every machine, and have not been tampered with in any way, misused, or suffered damage though accident, neglect, or conditions beyond Clausing Industrial’s control.

THERE ARE NO OTHER WARRANTIES, EXPRESSED OR IMPLIED, AND CLAUSING INDUSTRIAL SHALL NOT BE LIABLE UNDER ANY CIRCUMSTANCES FOR CONSEQUENTIAL DAMAGES.  Return of the Kalamazoo Saw Warranty Card within 10 days of installation shall serve as proof of installation of warranty coverage.

The KALAMAZOO SAW WARRANTY includes all parts and labor during the first twelve months of operation and replacement of parts only during the second year of operation.

CLAUSING/KALAMAZOO SAW is committed to continuous product improvement.  In keeping with this commitment, we reserve the right to change specifications and/or designs without notice or obligation.

FOB Point

Kalamazoo, Michigan or Point of Shipment.

Due to continual improvements, prices and specifications subject to change without notice.

Delivery

Delivery: ______ weeks, subject to prior sale.

Quote valid for 30 days.